## Slide 1
ESP32 with DHT11/DHT22 Temperature
and Humidity Sensor using Arduino IDE
ESP32와 DHT11 온/습도 센서
인터페이스 코드 설계
https://randomnerdtutorials.com/esp32-dht11-dht22-temperature-humidity-sensor-arduino-ide/
https://github.com/heartcom/ESP32

## Slide 2
DHT11 Vs. DHT22

## Slide 3
Schematic

## Slide 4
Installing Libraries  Adafruit library 사용

## Slide 5
Code 1/2
ESP32 with DHT11/DHT22 Temperature and Humidity Sensor using Arduino IDE | Random Nerd Tutorials
#include "DHT.h"
#define DHTPIN 4 // Digital pin connected to the DHT sensor
// Feather HUZZAH ESP8266 note: use pins 3, 4, 5, 12, 13 or 14 –
// Pin 15 can work but DHT must be disconnected during program upload.
// Uncomment whatever type you're using!
#define DHTTYPE DHT11 // DHT 11
//#define DHTTYPE DHT22 // DHT 22 (AM2302), AM2321
//#define DHTTYPE DHT21 // DHT 21 (AM2301)
// Connect pin 1 (on the left) of the sensor to +5V
// NOTE: If using a board with 3.3V logic like an Arduino Due connect pin 1
// to 3.3V instead of 5V!
// Connect pin 2 of the sensor to whatever your DHTPIN is
// Connect pin 4 (on the right) of the sensor to GROUND
// Connect a 10K resistor from pin 2 (data) to pin 1 (power) of the sensor
// Initialize DHT sensor.
// Note that older versions of this library took an optional third parameter to
// tweak the timings for faster processors. This parameter is no longer needed
// as the current DHT reading algorithm adjusts itself to work on faster procs.
DHT dht(DHTPIN, DHTTYPE);
void setup() {
Serial.begin(9600);
Serial.println(F("DHTxx test!"));
dht.begin();
}

## Slide 6
Code 2/2
ESP32 with DHT11/DHT22 Temperature and Humidity Sensor using Arduino IDE | Random Nerd Tutorials
void loop() {
// Wait a few seconds between measurements.
delay(2000); // Reading temperature or humidity takes about 250 milliseconds!
// Sensor readings may also be up to 2 seconds 'old' (its a very slow sensor)
float h = dht.readHumidity(); // Read temperature as Celsius (the default)
float t = dht.readTemperature(); // Read temperature as Fahrenheit (isFahrenheit = true)
float f = dht.readTemperature(true); // Check if any reads failed and exit early (to try again).
if (isnan(h) || isnan(t) || isnan(f)) {
Serial.println(F("Failed to read from DHT sensor!"));
return;
}
// Compute heat index in Fahrenheit (the default)
float hif = dht.computeHeatIndex(f, h); // Compute heat index in Celsius (isFahreheit = false)
float hic = dht.computeHeatIndex(t, h, false);
Serial.print(F("Humidity: ")); Serial.print(h);
Serial.print(F("% Temperature: ")); Serial.print(t); Serial.print(F("°C "));
Serial.print(f); Serial.print(F("°F Heat index: ")); Serial.print(hic); Serial.print(F("°C "));
Serial.print(hif); Serial.println(F("°F"));
}

## Slide 7
출력
ESP32 with DHT11/DHT22 Temperature and Humidity Sensor using Arduino IDE | Random Nerd Tutorials

## Slide 8
예제 코드의 문제점
DHT11의 저급한 성능 때문에 무조건 2초를 기다려야 한다.
이것 때문에 다른 일을 전혀 하지 못하게 된다.
이 문제를 해결하기 위하여 별도의 Timer를 사용하여 센서 값을 읽어 올 수 있다.
하지만, OS가 있다면 thread를 돌릴 수 있다.

## Slide 9
Install Library for ESPx  DHT SENSOR library for ESPx

## Slide 10
Code 1/6
#include "DHTesp.h" // Click here to get the library: http://librarymanager/All#DHTesp
#include <Ticker.h>
#ifndef ESP32
#pragma message(THIS EXAMPLE IS FOR ESP32 ONLY!)
#error Select ESP32 board.
#endif
/**************************************************************/
/* Example how to read DHT sensors from an ESP32 using multi- */
/* tasking. */
/* This example depends on the Ticker library to wake up */
/* the task every 20 seconds */
/**************************************************************/
DHTesp dht;
void tempTask(void *pvParameters); //pvParameters  pointer to void 포인터가 가리키는 대상이 정해지지 않은 포인터
bool getTemperature();
void triggerGetTemp();

## Slide 11
Code 2/6
/** Task handle for the light value read task */
TaskHandle_t tempTaskHandle = NULL;
/** Ticker for temperature reading */
Ticker tempTicker;
/** Comfort profile */
ComfortState cf;
/** Flag if task should run */
bool tasksEnabled = false;
/** Pin number for DHT11 data pin */
int dhtPin = 17;

## Slide 12
Code 3/6
/*** initTemp, Setup DHT library, Setup task and timer for repeated measurement
* @return bool  true if task and timer are started, false if task or timer couldn't be started */
bool initTemp() {
byte resultValue = 0;
dht.setup(dhtPin, DHTesp::DHT11);
Serial.println("DHT initiated");
// Start task to get temperature
xTaskCreatePinnedToCore(
tempTask, /* Function to implement the task */
"tempTask ", /* Name of the task */
4000, /* Stack size in words */
NULL, /* Task input parameter */
5, /* Priority of the task */
&tempTaskHandle, /* Task handle. */
1); /* Core where the task should run */
if (tempTaskHandle == NULL) {
Serial.println("Failed to start task for temperature update");
return false;
} else {
// Start update of environment data every 20 seconds  20초마다 triggerGetTemp() 함수 실행
tempTicker.attach(20, triggerGetTemp);
}
return true;
}

## Slide 13
Code 4/6
/*** triggerGetTemp , Sets flag dhtUpdated to true for handling in loop() , called by Ticker getTempTimer */
void triggerGetTemp() {
if (tempTaskHandle != NULL) {
xTaskResumeFromISR(tempTaskHandle);
}
}
/*** Task to reads temperature from DHT11 sensor * @param pvParameters * pointer to task parameters */
void tempTask(void *pvParameters) {
Serial.println("tempTask loop started");
while (1) // tempTask loop
{
if (tasksEnabled) {
// Get temperature values
getTemperature();
}
// Got sleep again
vTaskSuspend(NULL);
}
}

## Slide 14
Code 5/6
bool getTemperature() {
// Reading temperature for humidity takes about 250 milliseconds!
// Sensor readings may also be up to 2 seconds 'old' (it's a very slow sensor)
TempAndHumidity newValues = dht.getTempAndHumidity();
// Check if any reads failed and exit early (to try again).
if (dht.getStatus() != 0) {
Serial.println("DHT11 error status: " + String(dht.getStatusString()));
return false;
}
float heatIndex = dht.computeHeatIndex(newValues.temperature, newValues.humidity);
float dewPoint = dht.computeDewPoint(newValues.temperature, newValues.humidity);
float cr = dht.getComfortRatio(cf, newValues.temperature, newValues.humidity);
String comfortStatus;
switch(cf) {
case Comfort_OK:
comfortStatus = "Comfort_OK";
break;
case Comfort_TooHot:
comfortStatus = "Comfort_TooHot";
break;
~~~~~~~~~ 이하 생략

## Slide 15
Code 6/6
void setup()
{
Serial.begin(115200);
Serial.println();
Serial.println("DHT ESP32 example with tasks");
initTemp();
// Signal end of setup() to tasks
tasksEnabled = true;
}
void loop() {
if (!tasksEnabled) {
// Wait 2 seconds to let system settle down, 전원 인가 후 단 한번만 2초 대기.
delay(2000);
// Enable task that will read values from the DHT sensor
tasksEnabled = true;
if (tempTaskHandle != NULL) {
vTaskResume(tempTaskHandle);
}
}
yield();
}

## Slide 16
시험 결과

## Slide 17
ESP32 DHT11/DHT22 Web Server
Temperature and Humidity using Arduino IDE
https://randomnerdtutorials.com/esp32-dht11-dht22-temperature-humidity-web-server-arduino-ide/
Asynchronous ESP32 web serve를 만들고, DHT11 온도, 습도를 모니터링
Arduino IDE사용
온, 습도 값은 자동 refresh

## Slide 18
Install Library
https://github.com/adafruit/Adafruit_Sensor
https://github.com/adafruit/DHT-sensor-library

## Slide 19
Code 1/5
/********* Rui Santos Complete project details at https://randomnerdtutorials.com *********/
#include "WiFi.h"
#include "ESPAsyncWebServer.h"
#include <Adafruit_Sensor.h>
#include <DHT.h>
// Replace with your network credentials
const char* ssid = "REPLACE_WITH_YOUR_SSID";
const char* password = "REPLACE_WITH_YOUR_PASSWORD";
#define DHTPIN 27 // Digital pin connected to the DHT sensor
#define DHTTYPE DHT11 // DHT 11
//#define DHTTYPE DHT22 // DHT 22 (AM2302)
//#define DHTTYPE DHT21 // DHT 21 (AM2301)
DHT dht(DHTPIN, DHTTYPE);
// Create AsyncWebServer object on port 80
AsyncWebServer server(80);

## Slide 20
Code 2/5
String readDHTTemperature() {
// Sensor readings may also be up to 2 seconds 'old' (its a very slow sensor)
// Read temperature as Celsius (the default)
float t = dht.readTemperature(); // Read temperature as Fahrenheit (isFahrenheit = true)
if (isnan(t)) {
Serial.println("Failed to read from DHT sensor!");
return "--";
} else {
Serial.println(t); return String(t);
}
}
String readDHTHumidity() {
// Sensor readings may also be up to 2 seconds 'old' (its a very slow sensor)
float h = dht.readHumidity();
if (isnan(h)) {
Serial.println("Failed to read from DHT sensor!");
return "--";
} else {
Serial.println(h);
return String(h);
}
}

## Slide 21
Code 3/5
const char index_html[] PROGMEM = R"rawliteral(
<!DOCTYPE HTML><html>
<head>
<meta name="viewport" content="width=device-width, initial-scale=1">
<link rel="stylesheet" href="https://use.fontawesome.com/releases/v5.7.2/css/all.css" integrity="sha384-fnmOCqbTlWIlj8LyTjo7mOUStjsKC4pOpQbqyi7RrhN7udi9RwhKkMHpvLbHG9Sr" crossorigin="anonymous">
<style>
html { font-family: Arial; display: inline-block; margin: 0px auto; text-align: center; }
h2 { font-size: 3.0rem; }
p { font-size: 3.0rem; } .units { font-size: 1.2rem; } .dht-labels{ font-size: 1.5rem; vertical-align:middle; padding-bottom: 15px; }
</style>
</head>
<body>
<h2>ESP32 DHT Server</h2>
<p> <i class="fas fa-thermometer-half" style="color:#059e8a;"></i> <span class="dht-labels">Temperature</span>
<span id="temperature">%TEMPERATURE%</span> <sup class="units">&deg;C</sup> </p>
<p> <i class="fas fa-tint" style="color:#00add6;"></i> <span class="dht-labels">Humidity</span>
<span id="humidity">%HUMIDITY%</span> <sup class="units">&percnt;</sup> </p>
</body>
<script>
setInterval(function ( ) {
var xhttp = new XMLHttpRequest();
xhttp.onreadystatechange = function() {
if (this.readyState == 4 && this.status == 200) {
document.getElementById("temperature").innerHTML = this.responseText;
}
};
xhttp.open("GET", "/temperature", true);
xhttp.send();
}, 10000 ) ;

## Slide 22
Code 4/5
setInterval(function ( ) {
var xhttp = new XMLHttpRequest();
xhttp.onreadystatechange = function() {
if (this.readyState == 4 && this.status == 200) {
document.getElementById("humidity").innerHTML = this.responseText;
}
};
xhttp.open("GET", "/humidity", true); xhttp.send();
}, 10000 ) ;
</script>
</html>)rawliteral";
// Replaces placeholder with DHT values
String processor(const String& var){
//Serial.println(var);
if(var == "TEMPERATURE"){
return readDHTTemperature();
}
else if(var == "HUMIDITY"){
return readDHTHumidity();
}
return String();
}

## Slide 23
Code 5/5
void setup(){
Serial.begin(115200);
dht.begin();
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
delay(1000);
Serial.println("Connecting to WiFi..");
} // Print ESP32 Local IP Address
Serial.println(WiFi.localIP()); // Route for root / web page
server.on("/", HTTP_GET, [](AsyncWebServerRequest *request){
request->send_P(200, "text/html", index_html, processor);
});
server.on("/temperature", HTTP_GET, [](AsyncWebServerRequest *request){
request->send_P(200, "text/plain", readDHTTemperature().c_str());
});
server.on("/humidity", HTTP_GET, [](AsyncWebServerRequest *request){
request->send_P(200, "text/plain", readDHTHumidity().c_str());
});
server.begin();
}
void loop(){ }

## Slide 24
결과
Arduino
Web

## Slide 25
앞의 예제에서 html code를 index.html로 분리해보자.
폴더구조
project folder
data
index.html
index.html

## Slide 26
file 분리  기존 Arduino 파일에서 html 부분을 잘라내어 index.html 파일 생성
index.html  기존 코드에서 수정할 부분
1. CSS Link
<link rel="stylesheet" href="https://use.fontawesome.com/releases/v5.7.2/css/all.css">

## Slide 27
Arduino file 수정
index.html  기존 코드에서 수정할 부분
1. header file 추가
#include "FS.h"
#include "SPIFFS.h"
FS.h : file system interface 를 제공하는 파일 시스템 라이브러리
SPIFFS.h : ESP32 플래시 메모리에 파일을 저장할 수 있도록 설계된 라이브러리
2. setup() 함수에서 SPIFFS 시작
if(!SPIFFS.begin(true)){
Serial.println("SPIFFS Init Fail.");
return;
}

## Slide 28
Arduino file 수정
3. setup() 함수에서 web page 경로 수정
// Route for root / web page
server.on("/", HTTP_GET, [](AsyncWebServerRequest *request){
//request->send_P(200, "text/html", index_html, processor);
request->send(SPIFFS, "/index.html", "text/html");
});
server.on("/temperature", HTTP_GET, [](AsyncWebServerRequest *request){
request->send(200, "text/plain", readDHTTemperature().c_str());
});
server.on("/humidity", HTTP_GET, [](AsyncWebServerRequest *request){
request->send(200, "text/plain", readDHTHumidity().c_str());
});

## Slide 29
ESP32 Sketch Data Upload Tool 설치
ESP32FS Plug-in download
다운로드 받은 파일에서 esp32fs.jar 파일을 Arduino IDE tools 폴더에 복사
Windows: C:\Users\<사용자이름>\Documents\Arduino\tools Arduino를 program files 에 설치한 경우  C:\Program Files (x86)\Arduino\tools\ESP32FS\tool
Releases · me-no-dev/arduino-esp32fs-plugin

## Slide 30
ESP32 Sketch Data Upload Tool 설치
3. Arduino 종료 후, 재 실행
4. 툴  ESP32 Sketch Data Upload 메뉴 생겼는지 확인.

## Slide 31
ESP32 Sketch Data Upload Tool 설치
5. ESP32 Sketch Data Upload 클릭 ESP32 플래시 파일 시스템에 파일 업로드 시작( .html, .css, .js, .json 등 web resource file 을 SPIFFS에 저장)
6. Uploader 버튼 클릭

## Slide 32
동작